## Slide 1
Problem 1 — Answering the requirements directly (indicative numbers)
Requirement
Naive fully-automated SDL
This proposal (two-tier, human-in-the-loop)
High- throughput
Bottlenecked anyway: probing/anneal robotics limit end-to-end rate
Fast tier: 10–15 structural fingerprints/day + in-situ data every cycle (runs 24/7 unattended). Expensive tier: ~2x fewer electrical tests per insight (shown in silico) — effective throughput is measured in insights/month, not wafers/day
Footprint
150–250 m2 vacuum-integrated cluster + custom transfer robotics
One lab bay, ~60–80 m2: ALD + in-situ ellipsometry, XRR/GIXRD, RTP, probe station — all standard commercial tools, no custom integration
Cost
$8–15M class, 3+ years of robotics integration before first value (cf. Ada: ~$8M for one property)
$1.5–2.5M capex + 2–3 FTE. No bespoke robotics in Phases 0–1; automation added in Phase 2 only where data proves it pays
Period
Value arrives only after full integration succeeds
Phase 0 (6 mo): decision engine validated on existing/retrospective data. Phase 1 (by month 12–18): first virtual-metrology model + mapped process window — each phase delivers standalone value
Numbers are indicative planning estimates for discussion (tool list & vendor quotes in backup) — the design choice they reflect: spend capital on measurements and intelligence, not on robotizing steps a human does better during R&D.

## Slide 2
Problem 1 — From SDL to the fab: what Samsung gets beyond one material
The SDL's product is not a hero film — it is a TRANSLATOR (fast optical/structural data -> electrical performance) plus a map of where that translator is valid. That is fab language: virtual metrology.
1 · R&D acceleration (now)
• 2x fewer electrical-test cycles to a mapped process window (in-silico result) — directly shortens dielectric screening campaigns
• Candidates arrive with confidence labels, not just best guesses — fewer surprises downstream
2 · Pilot-line transfer (next)
• The trained translator deploys against inline ellipsometry/XRR that production lines already run on every wafer
• Validity map tells engineers WHEN inline data can replace destructive electrical/TEM sampling — and when it cannot (risk control, not just prediction)
3 · Compounding data asset
• Every sample carries full provenance: recipe -> tool logs -> fingerprint -> anneal -> electrical
• Dataset + models transfer to the next dielectric program (doped HfO2, FE-HZO, new precursors) — the asset outlives any single target spec
Where it lands (examples)
• DRAM capacitor dielectrics: EOT scaling needs new doped ZrO2/HfO2 stacks every node
• GAA / advanced logic gate stacks: interface + leakage co-optimization
• FE-HZO memory: wake-up/endurance vs anneal — same two-tier problem
• Same engine, new objectives: only the metrology list changes
KPI view (how I would be measured): electrical-test wafers per learned process window (target: -50%); time from 'new candidate material' to 'mapped safe operating window' (target: months, not years); fraction of routine electrical tests replaced by trusted virtual metrology (target grows every quarter); dataset reuse across programs (second program should start at ~30% lower cost).
This is the industrialization argument: the algorithm is the cheap part — the durable value is a validated translator + provenance-complete data, both of which plug into existing fab practice (inline metrology, APC/FDC), no new fab hardware required.

## Slide 3
Problem 1 — Risks I have designed for (and what stays honest)
Tool drift & metrology noise can mimic physics
Scheduled reference depositions + 2 process replicates per batch; noise is an explicit, learned term in the model. In the benchmark, removing replicates collapsed hidden-zone detection to chance — this is load-bearing, not bookkeeping.
Probe/anneal automation is where thin-film SDLs die
Human-in-the-loop tier + pre-patterned test substrates / Hg probe from day one. Robotics only in Phase 2, only where Phase-1 data proves the ROI.
Lab test structure is not the device stack
Position outputs as candidate windows; Phase-2 transfer validation on device-representative stacks before any claim reaches a product team.
Algorithm can lock in on a wrong 'untrustworthy' label
Found in silico: an early wrong noise estimate can freeze exploration. Fixed with an exploration safeguard (one random pick per batch). Cost to find it in simulation: days. In the lab: months.
Deposition temperature changes are slow (30-60 min stabilization)
Cost-aware scheduling batches experiments by thermal budget — the optimizer pays a modeled price for temperature moves.
The honest boundary: the in-silico result validates the decision engine, not the material physics — the first Phase-1 milestone is measuring the real fingerprint-to-electrical signal strength.

## Slide 4
Problem 2 — The three requirements map to three architectural decisions
REQ 1 · Individual AND integrated operation
• Hierarchical control planes: device layer -> per-SDL orchestrator -> fleet layer. Each SDL is fully functional standalone; the fleet layer only coordinates.
• Shared modules (robot arms, furnaces, analyzers) are RESOURCES with a reservation-based scheduler — no workflow owns a device, it books capabilities.
• Graceful degradation: if the fleet layer is down, every SDL keeps running its local queue. Integration is additive, never a dependency.
• Fab analogy: this is MES + equipment-level control, the pattern Samsung already trusts at scale — applied to research labs.
REQ 2 · Usable by non-SDL experts
• Researchers compose CAPABILITIES, not devices: a no-code canvas of verbs ('anneal at 500 C', 'measure thickness') — the scheduler resolves which physical tool executes.
• Recipe templates per domain (thin film, battery, organic): start from a working experiment, edit parameters, not code.
• Dry-run by default: every workflow executes first against the digital twin (simulated devices) — errors surface before hardware moves.
• Safety interlocks & approval gates are declared in the device contract, enforced by the orchestrator — not by user discipline.
REQ 3 · HW add/change/remove, minimal burden
• Device-plugin contract: a containerized driver + a machine-readable capability descriptor (verbs, parameter ranges, units, safety limits, calibration state).
• Register -> everything updates automatically: scheduler sees a new resource, GUI auto-generates its panel, provenance logging attaches — zero orchestrator code changes.
• Workflows bind to capabilities, not device IDs: swapping a furnace vendor is a config change; no workflow is rewritten.
• Versioned configs + twin regression test before a changed device re-enters production use.
One sentence: standardize the CONTRACT (capability descriptor + communication grammar), containerize the drivers, centralize only scheduling and data — then labs scale like fleets, not like one-off projects.
Standards I would build on rather than reinvent: SiLA2 / OPC-UA for lab devices (the 'SECS/GEM of the lab'), gRPC for transport, containerized microservices per module.

## Slide 5
Problem 2 — 'Minimal burden' made concrete: a new instrument joins in ~1 day
1 · Wrap
• Vendor driver goes into a standard SDK container — whatever the tool speaks (RS-232, Modbus, TCP, vendor DLL), the container's outward face is the universal grammar.
2 · Declare
• Capability descriptor (YAML): verbs it offers, parameter ranges & units, timing, safety limits, consumables, calibration schedule. This file IS the integration.
3 · Register
• Container announces itself to the orchestrator. Scheduler now sees a new bookable resource; data layer attaches provenance logging automatically.
4 · Verify
• Digital-twin dry-run + supervised first runs (shadow mode). Device is 'trusted' only after passing — same discipline as fab equipment qualification.
5 · Use
• GUI panel auto-generated from the descriptor; existing workflows that request matching capabilities can now be scheduled onto it. No workflow rewrites anywhere.
Why this is the industrially credible answer: integration cost is the #1 reason lab-automation programs stall. Making the capability descriptor the single integration artifact converts 'integration projects' (weeks of bespoke code, one engineer per instrument) into 'configuration work' (one file + one container). It also future-proofs the fleet:
removal is just deregistration (scheduler routes around it); replacement is a descriptor diff; upgrades are versioned and twin-tested before re-entering service — the same lifecycle discipline fabs apply to production equipment, scaled down to research.
This slide operationalizes the microservice diagram: the architecture is the same — this is the day-in-the-life proof that the burden is actually minimal.

## Slide 6
Problem 2 — The two hard problems under the hood: shared-resource scheduling & data
Scheduling shared modules (the real multi-SDL problem)
• Reservation-based allocation: workflows request capability + time window; the scheduler books physical resources — shared robot arms and furnaces stop being collision points.
• Priorities & preemption policy: campaign deadlines, maintenance windows, and calibration runs coexist by policy, not by hallway negotiation.
• Deadlock avoidance: all-or-nothing resource acquisition per workflow step (no workflow holds the robot while waiting for a busy furnace).
• Fairness across SDLs: per-lab budgets/quotas so one hot project cannot starve the others.
• Failure containment: a faulted device is quarantined; queued steps re-route to equivalent capabilities or pause cleanly — the fleet never cascades.
One data backbone for every SDL (thin film, battery, organic...)
• Sample-centric provenance graph: recipe -> device logs -> measurements -> model decisions — one queryable record per sample, across labs and modalities.
• Shared schema, domain-specific vocabularies: units, materials, and method ontologies per domain plug into one common core — integration without forcing uniformity.
• Streaming telemetry with drift alarms: FDC-style monitoring for research tools (reference-run tracking catches drift before it poisons a campaign).
• Decisions are data too: every algorithm suggestion is logged with model version + inputs — full auditability, reproducible campaigns, and the training corpus for the next generation of models.
• This is the asset that compounds: hardware depreciates; the provenance-complete dataset and the models trained on it appreciate.
Positioning: the GUI and microservices make the system usable; the scheduler and the data backbone make it an INSTITUTIONAL capability — multiple labs, one operational discipline, one growing asset. That is the difference between a lab demo and infrastructure a company runs for ten years.
Both components are deliberately boring technology (reservation schedulers, message queues, versioned schemas) — novelty lives in the decision algorithms, reliability lives here.