## Slide 1
the high-k layer, engineered by data
WORKFLOW PROPOSAL
A Self-Driving Laboratory for High-k Thin Films
Learning structure–property maps of ALD-grown dielectrics with the fewest possible experiments
[Your name] · [Affiliation]
Prepared for Samsung · July 2026 · Confidential draft

## Slide 2
MOTIVATION
High-k development is rate-limited by measurement, not deposition
2
Self-Driving Lab for High-k Thin Films — proposal draft
▸ Vast design space. HfO₂/ZrO₂-family stacks are tuned by composition, doping, cycle ratios, deposition temperature, plasma conditions, and anneal — a combinatorial space no grid study can cover.
▸ The properties that matter are slow to measure. Dielectric constant (k), leakage, and breakdown require electrodes, annealing, and probing: hours to days per sample.
▸ Fast measurements exist — but measure the wrong thing. Ellipsometry, XRR, and XRD take minutes yet report structure, not electrical performance.
▸ Blind sampling wastes the expensive tier. Most electrical tests land on samples that teach us nothing new about the process window.
The two-tier cost asymmetry
TIER 1 — Structural fingerprint (minutes)
Spectroscopic ellipsometry · XRR · GIXRD
Non-destructive, automatable, every sample
TIER 2 — Electrical truth (hours–days)
Anneal → electrodes → C–V and I–V probing
Gives k, leakage, breakdown — the real objective
Expensive, delicate, human skill required
Key message The scarce resource is the electrical measurement — so that is what an intelligent laboratory must spend wisely.

## Slide 3
PROPOSAL
A different kind of SDL: an efficient data engine, not a hero-film hunter
3
Self-Driving Lab for High-k Thin Films — proposal draft
Conventional SDL framing
Objective: autonomously find the single best film.
Optimizer converges, then the dataset is a by-product.
Result transfers poorly when the target spec changes.
This proposal
Objective: learn the map (process, anneal, structure) → (k, leakage) — and the boundaries of where that map is valid.
Every expensive electrical test is chosen by an algorithm to be maximally informative.
The model itself is the product: reusable for any future spec.
▸ Virtual metrology. Once trained, a 2-minute optical scan predicts k and leakage — electrical probing becomes the exception, not the routine.
▸ Validity mapping. The model reports where fast measurements reliably predict electrical behavior, and flags regions where hidden variables (phase mixture, interface layers) take over — exactly where the interesting physics and reliability risks live.
Key message We treat expensive characterization as a scarce resource allocated by an information-gain policy — value that survives any change of material target.

## Slide 4
PLATFORM
ALD is the most automation-ready synthesis tool in the fab
4
Self-Driving Lab for High-k Thin Films — proposal draft
The run is already digital
An ALD recipe is a parameter file: pulse/purge times, temperature, plasma power, cycle count.
Optimizer → recipe file → tool: no new robotics needed for synthesis.
Composition is software
Hf:Zr ratio and dopant level set by supercycle cycle ratios — an integer in the recipe.
No new solutions, targets, or precursor swaps to explore composition.
In-situ metrology for free
In-chamber ellipsometry / QCM give growth-per-cycle and film data every run, without unloading.
A fast autonomous inner loop with zero sample handling.
Proven starting point
Autonomous ALD process tuning with in-situ feedback has been demonstrated (e.g., Argonne National Laboratory). This proposal extends autonomy from process parameters to film properties — k and leakage — which no published SDL has closed the loop on.
▸ Honest constraint: one run = one composition (uniformity is ALD's virtue). We compensate with sample-efficient algorithms and rich in-situ data — not brute-force throughput.
Key message Spin-coating SDLs had to build the automation; an ALD SDL only has to connect what already exists — and add the intelligence.

## Slide 5
ARCHITECTURE
Two nested loops around one decision engine
5
Self-Driving Lab for High-k Thin Films — proposal draft
PLAN
active-learning engine picks next recipe
DEPOSIT
ALD · recipe-as-code supercycles
FAST METROLOGY
SE · XRR · GIXRD — minutes, every sample
INNER LOOP — fully autonomous, ~minutes
ESCALATE?
info gain vs cost
ANNEAL
RTP · thermal budget as model input
ELECTRICAL TEST
C–V · I–V on pre-patterned substrates — human-executed
MODEL UPDATE
structure→property map + uncertainty
OUTER LOOP — algorithm-selected samples only, human-in-the-loop
expert judgment where robots fail
DATA BACKBONE every sample carries full provenance: recipe → tool logs → structural fingerprint → anneal → electrical result · drift-control reference runs scheduled automatically

## Slide 6
DECISION ENGINE
Multi-fidelity active learning that knows what it doesn't know
6
Self-Driving Lab for High-k Thin Films — proposal draft
▸ Model. Probabilistic map from structural fingerprint + anneal parameters to k and leakage, with calibrated uncertainty (multi-fidelity Gaussian-process family).
▸ Acquisition. Chooses the next recipe AND whether a sample earns escalation to electrical testing — maximizing information gain per unit cost, with the human's time in the cost model.
▸ Two kinds of uncertainty, two actions. "Model needs more data" → sample nearby. "Fast measurements cannot resolve this region" → flag for deep analysis (TEM/XPS): hidden-variable physics found automatically.
▸ Drift-aware by design. Scheduled reference depositions and replicate measurements separate real materials physics from tool drift and metrology noise.
Validated before hardware
In-silico benchmark (month 0–6)
Synthetic HfO₂/HZO landscape built from literature (thickness–anneal–phase–leakage behavior).
Target: reach a fixed map accuracy with ≥3× fewer electrical tests than grid or random sampling.
Why this matters
The algorithm is proven on a known ground truth before a single wafer is spent.
The same benchmark becomes the acceptance test for the physical system.
Key message Sampling is steered toward the boundaries where predictability changes — where blind grids waste 90% of their budget.

## Slide 7
DEMONSTRATION
Proof of mechanism: the decision engine already works in silico
7
Self-Driving Lab for High-k Thin Films — proposal draft
▸ Result (6 campaigns, identical 150-test budget): our policy reaches the baselines' final map accuracy with ~half the electrical tests, wastes 16% vs 30–35% of budget in the unlearnable zone, and detects that zone best (AUC 0.74).
▸ What this does NOT claim: the landscape is synthetic (literature-inspired). It validates the algorithm, not the material physics — and it surfaced two deployment musts: replicate measurements enable validity mapping; an exploration safeguard prevents noise-map lock-in.
Key message Physics aside — the engine demonstrably learns what is learnable, flags what is not, and spends human time where it counts.

## Slide 8
EXECUTION
A phased roadmap where every stage delivers standalone value
8
Self-Driving Lab for High-k Thin Films — proposal draft
PHASE 0 · Months 0–6
Foundations
Data infrastructure & provenance schema
Retrospective modeling on existing ALD data
In-silico algorithm benchmark
Deliverable: validated decision engine + data backbone
PHASE 1 · Months 6–18
Human-in-the-loop SDL
Automated recipes + fast structural loop
Algorithm-selected electrical tests, human-executed
First structure→property map for one material system
Deliverable: virtual-metrology model v1 + mapped process window
PHASE 2 · Months 18+
Closing the loop
Automated sample handling & annealing integration
Expanded palette: dopants, laminates, electrodes
Transfer validation on device-representative stacks
Deliverable: autonomous platform + reusable materials dataset
▸ De-risked by design: if Phase 2 automation slips, Phases 0–1 have already delivered the dataset, the trained models, and the process windows — the scientific value does not depend on full autonomy.

## Slide 9
OUTCOME
What Samsung gets — and how we handle what can go wrong
9
Self-Driving Lab for High-k Thin Films — proposal draft
Virtual metrology
Predict k and leakage of new high-k films from a minutes-long optical scan — with quantified confidence and known validity limits.
Mapped process windows
Safe operating boundaries (thickness, composition, thermal budget) with the failure mechanisms at each edge identified.
A compounding dataset
FAIR, provenance-complete recipe→structure→electrical data — reusable for every future dielectric program and model.
Risks we have designed for
⚠ Tool drift & noise mimic physics — scheduled reference runs + replicates; noise terms explicit in the model
⚠ Probe automation is fragile — human-in-the-loop tier + pre-patterned test substrates from day one
⚠ Lab optimum ≠ device stack — Phase 2 transfer validation on device-representative structures
⚠ Temperature changes are slow — cost-aware scheduling batches experiments by thermal budget
Key message A laboratory that learns where measurements can be trusted — and spends human expertise only where it is irreplaceable.